## Slide 1
Disassembly Manual

## Slide 2
Disassembly Tools
Tweezers
Suction cup
SIM eject pin
Disassemble machine piece
Cross screwdriver – model no:LA61322P2+PH00

## Slide 3
Use a card retrieval needle to remove the SIM tray and memory tray.
STEP 1

## Slide 4
Remove the bottom screw* 2 pcs.
STEP 2

## Slide 5
STEP 3
In this incision direction, first use the dismantling machine piece in the corner to insert the top open a little, and then use the dismantling machine to cut open the surrounding buckle, open the back cover.

## Slide 6
STEP 4
Remove the motherboard bracket and the horn assembly screws.

## Slide 7
STEP 5
Remove the main board bracket/ speaker assembly/ single speaker.
Speaker

## Slide 8
STEP 6
Disconnect the side key FPC connector \ three-in-one FPC connector \ battery FPC connector, coaxial seat, front camera FPC connector(The front camera can be removed).
coaxial seat
battery FPC connector
Three in one FPC connector
Three in one FPC connector
Side key FPC connector
the front camera FPC connector
Main Mic: Welded on the sub-board, unable to be further disassembled.

## Slide 9
Remove the motherboard from the headset seat
STEP 7
External audio connectors:
Welded on the sub-board, unable to be further disassembled.
Disassemble the rear camera FPC

## Slide 10
STEP 8
Remove SUB-board and coaxis.
External charging port: Welded on the sub-board, unable to be further disassembled.

## Slide 11
Put the three-in-one module in the refrigerator for 20-30 minutes, then take out and knock out the battery.
STEP 9

## Slide 12
STEP 10
Place the whole unit face down on the heating plate and heat at 75°C for 5–8 minutes

## Slide 13
STEP 11
First, use a suction cup to grip the display and pull gently to create a small gap. Then insert an opening pick to pry it open slightly. Next, slide the opening pick around the edges to separate the adhesive. Finally, remove the TP.

## Slide 14
STEP 12
Remove earpiece, side key (Mechanical buttons), vibration motor, speaker FPC.
earpiece
side key
speaker FPC
vibration motor

## Slide 15
Assembly Manual

## Slide 16
Install receiver, side keys, thermal silicone, speaker FPC, and vibration motor.
Install light sensor sealing silicone sleeve and charging indicator light transparent silicone

## Slide 17
STEP 1
Assemble headphone jack sealing silicone sleeve and rear camera.

## Slide 18
STEP 2
Assemble USB sealing silicone sleeve and install coaxial cable.

## Slide 19
STEP 3
Attach shielding cover thermal graphite sheet

## Slide 20
STEP 4
Connect the side key FPC connector, three-in-one FPC connector, battery FPC connector, coaxial seat and front camera FPC connector
coaxial seat
battery FPC connector
Three in one FPC connector
Three in one FPC connector
Side key FPC connector
the front camera FPC connector

## Slide 21
STEP 5
Attach the NFC antenna as shown in the figure

## Slide 22
STEP 6
Install the mainboard bracket and speaker assembly (single speaker).
Speaker

## Slide 23
Peel off the release liner and fit the fingerprint module onto the battery cover

## Slide 24
STEP 7
Install the mainboard bracket and speaker assembly screws, engage the fingerprint module connector, then fit the battery cover.
Snap on the fingerprint module connector

## Slide 25
Remove the bottom screw* 2 pcs
STEP 8